About your Cavity Wax Injection

The purpose of this process is to coat as much of the internal surfaces of box sections as possible with a professional cavity wax product which repels water and excludes air from steel and thus hinders rusting. Box sections include sills, doors, bonnet gutters, outer/inner sill cavities, chassis members, subframes etc.

Cavity wax is designed to run into crevices and stay there, remaining flexible indefinitely. In the very long term it will evaporate but this would take at least 20 years – more in a sealed cavity.

KWE accesses some sealed cavities by means of drilling 9mm holes, and after injection the hole is plugged with a removable rubber blind grommet.

Cavity wax will not remove existing rust but will stop it progressing provided it is coating all surfaces. There will be some places where this is impossible to achieve, for example at the edge of wheel arch lips where cavity wax would be unsightly and would get washed off. In these cases KWE will coat the areas with a harder underseal compound though it is still vulnerable to aggressive washing.

You can expect the smell of cavity wax to linger for some weeks depending on how well ventilated the car is. In high concentrations the vapour is harmful so please be sure to have the aircon blowing hard or the windows partly open when driving a freshly processed car.

There may be some drips of cavity wax from underside drains – e.g. doors and sills – which may discolour brick drives. This will be accelerated in hot weather but should cease within a few weeks as the product partly hardens. The product can be removed with white spirit, paraffin or petrol (with care)!

KWE is careful to protect the paintwork and interior trim from the cavity wax, but there may be patches we’ve missed in the final clean-up. No harm will be done to trim and paint so a gentle wipe with whiter spirit will suffice. We err on the side of too much product rather than too little.

Like any applied coating, a second coat is advisable within a couple of years. KWE will carry out this second coating for substantially less than the first application since there will be no drilling required.

We provide this injection process in good faith and after long and successful experience; however we do not offer any guarantee that rust will not reappear or start in a new place. Steel has a fundamental propensity to rust, but this process definitely slows or stops the process.

End